## Slide 1: Mode: eth -> wan WiFi ->Ap

## Slide 2
sudo apt-get update && apt-get upgrade -y
sudo apt-get install dnsmasq hostapd

## Slide 3: nano /etc/dhcpcd.conf
interface wlan0
static ip_address=192.168.4.1/24

## Slide 4: nano /etc/network/interfaces
allow-hotplug wlan0
iface wlan0 inet manual

## Slide 5
sudo service dhcpcd restart

## Slide 6: nano /etc/hostapd/hostapd.conf
interface=wlan0
driver=nl80211
ssid=pi3_ap
hw_mode=g
channel=6
wmm_enabled=1
macaddr_acl=0
auth_algs=1
ignore_broadcast_ssid=0
wpa=2
wpa_passphrase=12345678
wpa_key_mgmt=WPA-PSK
rsn_pairwise=CCMP

## Slide 7: nano /etc/default/hostapd
DAEMON_CONF="/etc/hostapd/hostapd.conf"

## Slide 8: sudo mv /etc/dnsmasq.conf /etc/bak_dnsmasq.conf sudo nano /etc/dnsmasq.conf
interface=wlan0
bind-interfaces
server=8.8.8.8
domain-needed
bogus-priv
dhcp-range=192.168.4.2,192.168.4.254,12h

## Slide 9: sudo nano /etc/sysctl.conf
net.ipv4.ip_forward=1
sudo sh -c "echo 1 >/proc/sys/net/ipv4/ip_forward"

## Slide 10: routing
sudo iptables -t nat -A POSTROUTING -o eth0 -j MASQUERADE
sudo iptables -A FORWARD -i eth0 -o wlan0 -m state --state RELATED,ESTABLISHED -j ACCEPT
sudo iptables -A FORWARD -i wlan0 -o eth0 -j ACCEPT
sudo sh -c "iptables-save > /etc/iptables.ipv4.nat"

## Slide 11: nano /etc/rc.local
在exit 0 上面一行貼
iptables-restore < /etc/iptables.ipv4.nat

## Slide 12
sudo service hostapd start
sudo service dnsmasq start
sudo reboot

## Slide 13
Mode:2
Wifi ->wan
LAN->AP for eth0

## Slide 14
sudo apt-get install isc-dhcp-server

## Slide 15: nano /etc/dhcpcd.conf
interface eth0
static ip_address=192.168.4.1/24
static domain_name_servers=8.8.8.8

## Slide 16: nano /etc/default/isc-dhcp-server
INTERFACESv4="eth0“

## Slide 17: nano /etc/dhcp/dhcpd.conf
subnet 192.168.4.0 netmask 255.255.255.0 {
range 192.168.4.2 192.168.4.250; # 開放配發的 IP 範圍
option routers 192.168.4.1; # 預設通訊閘道
option broadcast-address 192.168.4.255; # 廣播位址
default-lease-time 600; # 預設租約時間，單位為秒
max-lease-time 7200; # 最長租約時間，單位為秒
option domain-name-servers 8.8.8.8; # DNS 伺服器
}

## Slide 18
/etc/init.d/isc-dhcp-server restart
echo 1 > /proc/sys/net/ipv4/ip_forward
iptables -A FORWARD -i eth0 -o wlan0 -j ACCEPT
iptables -A FORWARD -i wlan0 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
iptables –t nat -A POSTROUTING -o wlan0 -j MASQUERADE